# AlphaEcall™ 100 series Architectural and Engineering Specifications

Contractor shall furnish, and install the AlphaEcall™ 100 series Emergency Call System as manufactured by Alpha Communications®, 42 Central Drive, Farmingdale NY 11735-1202, Phone: 1-800-666-4800, www.AlphaCommunications.com, and any other necessary equipment required for complete system operation.

If AlphaEcall™ 100 series is to be used in conjunction with an outside Central Monitoring service, contractor shall furnish and install the model TAK-4202 Telephone Auto Dialer and/or any other equipment required for proper operation, and contractor shall install a dedicated phone line to accommodate this optional system capability. Phone line shall not require the use of a cable modem or other internet service in order for emergency calls to be placed.

Contractor shall be responsible to verify that the AlphaEcall™ 100 series service will be compatible with the building’s intercom/call system(s).

Contractor shall install in a suitable secure and environmentally suitable area, the AlphaEcall™ 100 series central equipment, and any other hardware and cabling required for incorporation into the system.

At each Master Annunciator location, contractor shall furnish and install the necessary AlphaEcall™ 100 series Master Annunciator station.

Contractor shall furnish, install and configure the AlphaEcall™ 100 series system as directed by architect/engineer/building owner/manager or developer in charge of the project.

Contractor shall provide instructions to necessary building personnel regarding the proper method of operation of the AlphaEcall™ 100 series system.

DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer’s instructions.

C.	Handling:  Protect materials during handling and installation to prevent damage.

LIMITED WARRANTY

A.	Warranty Period: Each piece of equipment supplied by Alpha Communications® and others shall be warranted by the manufacturer to be free of defects in material and workmanship for a period of 12 months from the date of shipment, as covered by the manufacturer’s Limited Warranty.

PROJECT CONDITIONS

- Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's absolute limits.

- Use factory recommendations regarding wiring type and gauge in order to insure proper system function and dependability. Also follow factory recommendations regarding distance limitations.

- When running wiring avoid proximity to AC wiring, fluorescent ballasts, dimmers, motors and compressors to prevent potential EMI issues that will affect proper operation of the system.

Any items not specified herein that is needed for proper operation will be included in this specification.

SYSTEM OPERATION REQUIREMENTS

System shall operate as follows:

SYSTEM CAPABILITIES

The AlphaEcall™ 100 series system shall be used to notify building staff and/or emergency personnel when a resident or visitor to the building needs assistance, by activation of an Emergency Call Station or device.

EMERGENCY CALL OPERATION

When a resident or visitor wishes to place an emergency call, he/she shall activate the closest Emergency Call Station (ECS) by pulling on a cord or pressing a call switch (or other type of activation from another compatible device such as a wireless pendant), depending on the type of ECS being utilized.

When an ECS is activated, one of several notifications shall occur; (1) An LED will light at each Master Annunciator Station that services the calling location, along with an audible tone signal, (2) a corridor dome light will light outside of the calling room location (with optional audible buzzer or horn), (3) a common Floor Bell (or similar device) shall sound, alerting neighbors on that floor to the emergency call, (4) an electric door strike will activate at the entry door to the calling location to allow neighbors and/or emergency personnel access to the apartment/suite and (5) one or more Remote Sounders shall sound an audible tone signal, (6) a common system relay shall activate allowing additional notification devices such as strobes, horns, bells, remote phone dialer, etc., (7) one or more Pocket Pagers shall activate and display the room number or location of the ECS that has been activated. NOTE: systems that use incandescent bulbs for call indication at the Master Annunciator Station shall not be acceptable.

The audible tone signal shall be able to be silenced from any of the Master Annunciator Stations or Remote Sounder Stations, by pressing the Tone Silence button.

Any and all “Emergency Calls” shall only be resettable at the original point of origin (or ECS).

EQUIPMENT REQUIRED

At each Master Annunciator Station location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one or more ‘MT’ series mounting trim frames (in Titanium, White or Brown finish – please specify) along with the associated ‘UPG’ series flush back box/housing or ‘APG’ series surface/desk back box/housing, a TSME tone speaker module (in matching finish to the ‘MT’ trim frame), and one or more ELM116 16-LED indicator modules. For desk mounting contractor shall furnish and install the necessary TZ1003 series desk adapter unit(s). For future service purposes contractor shall furnish a model 13510 key/tool which allows access to the Master Annunciator Station.

At each Remote Sounder location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) model RS101S surface mount Remote Sounder Station with included housing.

At each Emergency Calling location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) (or more) of the following Emergency Call Stations (ECS); SF117/2A Emergency Pull Station (with Red call placed window indicator and for activation for up to 2 options), SF117/4C Emergency Pull Station (with no call placed window indicator and for activation for up to 4 options), SF118/2C Emergency Pull Station (with Red LED call placed indicator and for activation for up to 2 options, SF118/4C Emergency Pull Station (with Red LED call placed indicator and for activation for up to 4 options, or SF154A Emergency Push Station (with Red call placed window indicator and for activation for up to 2 options). NOTE: Other types of ECS devices can be specified here as well, as needed.

At each Emergency Calling location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) CDL101LED (White LED) type Corridor Dome Light (with no audible sounder), or one (1) CDL101B (White LED) type 24vdc Corridor Dome Light (with built-in Piezo Buzzer), or one (1) CDL118B (White LED) type 24vdc Corridor Dome Light (with built-in Horn), or one (1) CDL123B (White LED) type 24vac Corridor Dome Light (with built-in Horn), depending on voltage requirements and as required for system functions. Corridor Dome Lights using incandescent bulbs shall not be acceptable.

(OPTION): At each Floor location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) BE005 24vac Floor Bell, or one (1) BE007 24vdc Floor Bell, depending on system voltage required.

At the Central Equipment location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) AC219 System Annunciator Controller and one (1) SS106 UL Listed Pigtail transformer. (OPTION): Contractor shall furnish and install a secure metal enclosure for the central equipment (model# CEC152 or equivalent).

(OPTION): At the Central Equipment location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; all components as required for the addition of an AlphaPage™ Pocket Paging system (with associated Pocket Pagers) to be added to the AlphaEcall™ 100 series system.

(OPTION): At the Central Equipment location, contractor shall furnish and install the following Alpha Communications® AlphaEcall™ 100 series system components; one (1) model TAK-4202 Remote Telephone Dialer, to be used to call an outside phone line in the event of an Emergency Call activation. Contractor shall connect the TAK-4202 to a dedicated (POTS) telephone line.

(OPTION): At the Central Equipment location, contractor shall furnish and install any necessary UPS, battery back-up, emergency generator, or other back-up power as required by local code and the Authority Having Jurisdiction (AHJ).

Revised 09/20/2018